## Slide 1
REVA UNIVERSITY | MACHINE LEARNING
County-level
high-burden
alert model
Three-hour horizon using EAGLE-I history and historical weather
Rohan Sai Gorumutchu
CSIT A | Semester 5 | SRN R24EJ042
Machine Learning Mini Project
DATA PERIOD
2014–2024
363,419
county/time forecast windows
2024 historical test
79.5% precision | 61.0% recall
Research result, not a live outage service
Notes: Student details retrieved from prior project chat. Dataset and metrics from the bundled project results.json and source_audit.json.

## Slide 2
A long history, with a strict time split
EAGLE-I county readings joined to historical station weather
Michigan outage research | Rohan Sai Gorumutchu | CSIT A
02
363,419
forecast windows
83
Michigan counties
67
model input features
2014–24
data coverage
Forecast windows by year
3.4k
2014
24.8k
2015
11.4k
2016
26.7k
2017
35.6k
2018
41.1k
2019
40.7k
2020
44.0k
2021
44.9k
2022
45.0k
2023
45.8k
2024
Train 2014–2022
Threshold: 2023
Test: 2024
2014 coverage begins on November 1, so that first training year is partial.
Weather archive coverage is seasonal (late May through August), not full-year.
Sources: EAGLE-I outage archive; Iowa Environmental Mesonet ASOS observations.
Notes: EAGLE-I annual source files were checksum-verified against the local Figshare metadata. Weather from 75 Michigan ASOS stations, spatially aggregated; archived seasonal window is approximately May 28 to September 1. Sources: https://doi.org/10.6084/m9.figshare.24237376 and https://mesonet.agron.iastate.edu/request/download.phtml

## Slide 3
How the model turns history into an alert
The target describes a high-burden county window, not the start of a household outage
Michigan outage research | Rohan Sai Gorumutchu | CSIT A
03
1 Align sources
Quarter-hour EAGLE-I county readings
Hourly ASOS weather observations
2 Clean & engineer
Complete-hour checks
Weather lags and storm codes
Past outage summaries and calendar
3 Label next 3 hours
County training-period 90th percentile
Positive if any next-hour count
reaches that county cutoff
4 Train & evaluate
Histogram Gradient Boosting
Threshold selected on 2023
Fixed historical test on 2024
Input groups
Weather
temperature, gust, precipitation, pressure
Storm signals
reported thunderstorm, squall, heavy rain
Outage history
recent count, 6–48 hour summaries, coverage
Context
county location, local hour, weekday, month
NWS warning records were omitted because verified year-complete warning data was unavailable.
Notes: Weather availability assumes a two-hour delay for observations; actual operational latency was not verified. Missing data remains missing and is handled natively by HistGradientBoosting.

## Slide 4
2024 test: strong precision, moderate event coverage
Threshold was fixed using 2023 only; scores are retrospective and uncalibrated
Michigan outage research | Rohan Sai Gorumutchu | CSIT A
04
Precision
79.5%
Recall
61.0%
F1 score
69.0%
Accuracy
93.8%
What those scores mean
3,980
model alerts among 45,804 test windows
815
false alerts
2,024
missed positives
Average precision
0.733
ROC AUC
0.889
Validation false-positive rate: 2.00% | 2024 test false-positive rate: 2.01%
Precision is the share of alerts that matched the high-burden label. Recall is the share of positive windows detected.
Notes: Metrics are from outputs/results.json. The 2024 period had been examined earlier in the project, so it is a reused historical holdout, not a pristine independent test. The 2% false-positive cap was selected on 2023 and is not guaranteed to transfer.

## Slide 5
Examples and what the model can support
Selected from the 2024 test by score alone; actual outcome shown for retrospective context
Michigan outage research | Rohan Sai Gorumutchu | CSIT A
05
Issue time (UTC)
County
Model score*
Prediction
Actual label
2024-06-26 06:00
Muskegon
0.998
Alert
High burden
2024-08-28 18:00
Clare
0.998
Alert
High burden
2024-06-26 09:00
Muskegon
0.998
Alert
High burden
2024-07-10 09:00
Allegan
0.774
No alert
No high burden
2024-03-09 03:00
Wayne
0.774
No alert
No high burden
2024-11-11 15:00
Marquette
0.774
No alert
High burden
* Uncalibrated model score; not a real-world outage probability.
Scope
County-level burden signal for the next 3 hours. It does not identify a household outage or cause.
Caveats
Coverage varies by year. Weather delay is assumed. 2014 is partial. The 2024 test was previously inspected.
Sources: EAGLE-I (Figshare) | Iowa Environmental Mesonet ASOS
Notes: Sources: EAGLE-I data archive, https://doi.org/10.6084/m9.figshare.24237376 ; Iowa Environmental Mesonet ASOS data request, https://mesonet.agron.iastate.edu/request/download.phtml . Source audit bundled in project: source_audit.json.